Survey Date:	5 December 2006

Nature of Survey:		Complete Survey

Report File (this document):  	HHWQMP_report118_061205.doc

Data File:		HHWQMP_data118_061205.xls

Data Return:

Profile:  		100%

Bacteria:  	100%

Chemical: 	100%

Overall:  	100%

Sample Notes:

The CTD QA/QC procedure indicates that there may be a relatively well-oxygenated shallow surface layer in Herring Cove that is missed in the processed data.

QA/QC samples:

| Chemical Analysis |  | EE2 - 10m |  |
| --- | --- | --- | --- |
| Detectable |  | reference |  |
| Parameter | units | sample | QA/QC |
| Ammonia (as N) | mg/L | 0.08 | 0.09 |
| Total Suspended Solids | mg/L | 1 | 2 |
| Copper | ug/L | 0.3 | 0.2 |
| Iron | ug/L | 16 | 14 |
| Lead | ug/L | 0.1 | <0.1 |
| Manganese | ug/L | 2 | 2 |
| Zinc | ug/L | <1 | 1 |

Fecal Coliform (CFU/100ml)

| Site | HC-10M | HP2-1M | HC-1M | EE2-10M |
| --- | --- | --- | --- | --- |
| Reference | 24 | 49 | 75 | 740 |
| QA/QC | 39 | 46 | 71 | 1200 |

Comments:

General:  There has been significant rainfall in the days prior to the survey.  Compared to two weeks ago, the northern Basin is more stratified with a fresher surface layer, particularly at sections H and western end of section F. The Inner Harbour is generally more saline and less stratified, particularly in the top 10m, than in the last survey.  The water temperature has dropped relatively uniformly by about 2( C.  There is a freshwater surface signature at HP2. The fecal coliform levels are everywhere quite high, including the Northwest Arm and Eastern Passage. In the Basin, the typical situation of higher FC values at 10m exists, except for in the fresher water lens at F1.  This suggests that the source of this freshwater lens may be the Fairview Cove outfall (Duffus street diversion).  In the Inner Harbour the FC values are anomalously quite vertically uniform.  Particularly unusual is the fact that at the EE section the 10m values are all higher than the 1m samples. The coliform values are significantly elevated in the Outer Harbour all the way to site B2. The site HP3 FC values are higher than the Herring Cove (HC) FC values.  This suggests that the FC source is the Tribune Head outfall not Herring Cove, but that the source of the freshwater at HP2 (lower FC) is likely HC.

Fluorescence:  Overall the fluorescence values are very low with profile maximum values of 1-2 mg/m3 everywhere, with values of 2 mg/m3, or slightly higher only in the southern Basin.

Ammonia:  Ammonia values are highest in the 1 m samples in the Narrows and southern Basin (0.12 mg/L) with values decreasing somewhat in all directions to non detectable levels (<0.05 mg/L) at B2.

TSS:  TSS values are relatively low (1.0-3.0 mg/L), with no apparent pattern.

Dissolved Oxygen: The data indicate that the dissolved oxygen (DO) in the deepest Basin bottom water has continued to drop from about 4.5 mg/L two weeks ago, to about 3.5mg/L, with levels below 4.5 mg/L everywhere deeper than 25 m. Elsewhere, the measured DO values are very uniform between 6-7 mg/L.  These values are below the guideline values in all SA (Outer Harbour) and SB (Basin, Northwest Arm, Eastern Passage) areas but are everywhere above the SC guidelines in the Inner Harbour. The DO data is not ground-truthed and absolute values are questionable (see DO discussion in QR#1).

# Text boxes

Yacht Clubs

Yacht Clubs

Rainfall and temperature data

collected at

Shearwater Autoport.

Cloud cover data collected at Shearwater Airport

Unless otherwise labeled:

- salinity contour interval is 0.5 PSU

- temperature contour interval is 0.5ºC.

Unless otherwise labeled:

- density contour interval is 0.2 kg/m3

Yacht Clubs

Rainfall and temperature data

collected at

Shearwater Autoport.

Cloud cover data collected at Shearwater Airport

Rainfall and temperature data

collected at

Shearwater Autoport.

Cloud cover data collected at Shearwater Airport

Rainfall and temperature data

collected at

Shearwater Autoport.

Cloud cover data collected at Shearwater Airport

LEGEND

= Ten Metre Sample

= One Metre Sample

RDL = Reportable Detection Limit