Survey Date:	20 December 2006

Nature of Survey:		Complete Survey

Report File (this document):  	HHWQMP_report119_061220.doc

Data File:		HHWQMP_data119_061220.xls

Data Return:

Profile:  		100%

Bacteria:  	100%

Chemical: 	100%

Overall:  	100%

Sample Notes:

CBOD samples were taken at 1 and 10 m at site F1.

The CTD QA/QC procedure indicates that there may be a relatively well-oxygenated shallow surface layer in Herring Cove that is missed in the processed data.

QA/QC samples:

| Chemical Analysis |  | G2-10m |  |
| --- | --- | --- | --- |
| Detectable |  | Reference |  |
| Parameter | Units | Sample | QA/QC |
| Ammonia (as N) | mg/L | <0.05 | <0.05 |
| Total Suspended Solids | mg/L | 2.5 | 2 |
| Copper | ug/L | 0.3 | 0.3 |
| Iron | ug/L | 6 | 5 |
| Manganese | ug/L | 2 | 1 |
| Zinc | ug/L | 1 | 1 |

Fecal Coliform (CFU/100ml)

| Site | H3-10m | EE1-1m | H1-10m | G2-10m |
| --- | --- | --- | --- | --- |
| Reference | 59 | 1300 | 20 | 47 |
| QA/QC | 65 | 1500 | 26 | 150 |

Comments:

## General:  The weather has been dry. The surface salinity is higher everywhere than two weeks ago and increases slowly from the head of the Basin to the Outer Harbour (1 PSU total) with a slight reduction in the Narrows, likely due to local sewage input. The water temperature in the top 20 m is relatively uniform at 5-6 C, about two degrees colder than last week.  The temperature in the Basin deep water is unchanged.  The fecal coliform values are relatively high in the Inner Harbour with the distribution displaced somewhat down harbour, probably due to the persistent moderate down Harbour winds. There are high fc values out to section C.  The vertical coliform distribution is for the most part typical.  There are elevated coliform values in the 1m samples at both the HC and HP1 sites.  Given the dry weather, the source is likely the Tribune Head outfall.

Fluorescence:  Overall the fluorescence values are very low with profile maximum values of about 1 mg/m3 everywhere. The highest values (1.8 mg/m3) occur at 5m in the Narrows.

Ammonia:  Ammonia values are again highest in the Narrows and southern Basin (about 0.10 mg/L) with detectable values in both the 1 and 10m samples. Everywhere else, detectable values  (>0.05 mg/L) only occur in the 1 m samples and decrease with increasing distance from the Narrows, dropping below detection limits by site B2.

TSS:  TSS values are generally relatively low (1.0-3.0 mg/L), however there are three higher values (3-7 – 6.4 mg/L) seemingly associated with lenses of less dense water in the Narrows and northern Basin.  These elevated values are not associated with anomalies in secchi depth.

Dissolved Oxygen: The data indicate that the dissolved oxygen (DO) in the deepest Basin bottom water has continued to drop from about 3.5 mg/L two weeks ago, to about 3.0 mg/L, with levels below 4.0 mg/L everywhere deeper than 30 m. The values are between 6-7 mg/L in the top 20m of the Basin and increase continuously to about 7.5 mg/L in the Outer Harbour. These values are below the guideline values in the SA (Outer Harbour) and the innermost parts of the SB (i.e. the Basin, and the Northwest Arm) areas, but are above the SC guidelines everywhere in the Inner Harbour. The DO data is not ground-truthed and absolute values are questionable (see DO discussion in QR#1).

CBOD:  The two samples at F1 showed non-detectable CBOD.

# Text boxes

Yacht Clubs

Yacht Clubs

Rainfall and temperature data

collected at

Shearwater Autoport.

Cloud cover data collected at Shearwater Airport

LEGEND

= Ten Metre Sample

= One Metre Sample

RDL = Reportable Detection Limit

Yacht Clubs

Rainfall and temperature data

collected at

Shearwater Autoport.

Cloud cover data collected at Shearwater Airport

Rainfall and temperature data

collected at

Shearwater Autoport.

Cloud cover data collected at Shearwater Airport

Rainfall and temperature data

collected at

Shearwater Autoport.

Cloud cover data collected at Shearwater Airport