Survey Date:	15 January 2009

Nature of Survey:		Complete Survey

Report File (this document):  	HHWQMP_report174_090115.doc

Data File:		HHWQMP_data174_090115.xls

Data Return:

Chemical: 	57%

Bacteria:  	52%

Profile:  		47%

Overall:  	51%

Sample Notes:

This is an abbreviated survey undertaken in response to the failure of the Halifax STP. Only the Inner Harbour, Southern Basin and NW Arm were sampled.

There was no YSI ground truth DO data collected, due to instrument unavailability.

The QAQC fecal coliform sample at PC-10 m was not collected.

QA/QC samples:

| Chemical Analysis |  | E2-1m |  |
| --- | --- | --- | --- |
| Detectable |  | Reference |  |
| Parameter | Units | Sample | QA/QC |
| Ammonia (as N) | mg/L | 0.42 | 0.07 |
| Total Suspended Solids | mg/L | 1 | 2 |
| Copper | ug/L | 0.4 | 0.4 |
| Iron | ug/L | 10 | 11 |
| Manganese | ug/L | 2 | 3 |
| Zinc | ug/L | 1 | 1 |

Fecal Coliform (CFU100ml)

| Site | E2-1m |
| --- | --- |
| Reference | 40 |
| QA/QC | 43 |

Comments:

General: There has been light rainfall (about 20 mm in total) in the five days before the survey.  Based on the limited CTD data the Inner Harbour is well mixed and quite uniform in most parameters.  There are some, but not many, elevated bacteria concentrations, in sections D and EE.

Fluorescence: The fluorescence data indicates minimal phytoplankton activity with values all < 2.0 mg/m3 or about annual minimum levels.

TSS: The TSS levels are relatively low with all but one concentration 3 mg/L or less and a mean of 2.2 mg/L.  There is one value of 7 mg/L at EE2-10 m.

Ammonia:  The ammonia levels are somewhat elevated, with detectable concentration in all samples and a mean value of about 0.12 mg/L.  The mean is skewed by a single relatively high value (0.42 mg/L) at E2 1 m in the Narrows.  This high level is not supported by the QAQC sample at the same site (see adjacent table).

Metals: There are no guideline exceedences. Copper concentrations are the closest to guideline exceedence with several sample concentrations of about 20 - 25% of the 2.9 ug/L guideline.

Dissolved Oxygen: There is no YSI ground truth data for this survey (see sample notes).  The CTD measured DO levels are very uniform at about 6.8 mg/L.  The scale factor has been stable at 1.4 over the previous few surveys.  This would suggest that the DO levels are about 9.5 mg/L.  This is consistent with measurements made by BBPMP and the LOBO buoy (see data file).  The BBMP data indicate that the DO at the bottom of Bedford Basin continues to drop and is now less than 4 mg/L.

# Text boxes

Yacht Clubs

Yacht Clubs

Rainfall and temperature data

collected at

Shearwater Autoport.

Cloud cover data collected at Shearwater Airport

LEGEND

= Ten Metre Sample

= One Metre Sample

RDL = Reportable Detection Limit

Yacht Clubs

Rainfall and temperature data

collected at

Shearwater Autoport.

Cloud cover data collected at Shearwater Airport

Rainfall and temperature data

collected at

Shearwater Autoport.

Cloud cover data collected at Shearwater Airport

Rainfall and temperature data

collected at

Shearwater Autoport.

Cloud cover data collected at Shearwater Airport